Eastern bluebird populations have been reduced by up to 90% over the last few decades – partly  due to a lack of suitable nesting places. To help restore the population of these beautiful birds, the East Ascension Sportsman’s League has built & distributed over 1000 specially designed nesting boxes. You can help to, by building and properly installing this simple nest box.

Materials of construction:  rough-cut red cedar & galvanized nails

,              =  nail locations (14 total nails per box)

# Text boxes

EASL Bluebird Nest Box Design

Side View

Front View

15o angle cuts

30o angle cut

1 1/2”

Floor piece intentionally cut too short.
Leave gap in back.

Total floor dimensions should be no less than 4” x 4”.

Ventilation/Drainage

The bottom of the
1 1/2” hole must be a minimum of 6” from the floor.

To allow front door to swing open, use only  2 nails to hold front in place; center nails with hole

Recess floor upward - slightly.

Front

Bottom View